INSTALLATION AND SAFETY INSTRUCTIONS

FOR YOUR SAFETY WARNING

BE SURE THE ELECTRICITY TO THE WIRES YOU ARE WORKING ON IS SHUT OFF; EITHER THE FUSE IS REMOVED OR THE CIRCUIT BREAKER IS SHUT OFF. GENERAL You don’t need special tools to install this fixture. Be sure to follow the steps in the order given. Under no circumstances should a fixture be hung on house electrical wires, nor should a swag type fixture be installed on a ceiling which contains a radiant type heating system. Read instructions carefully. If you are unclear as to how to proceed, consult a qualified electrician. NOTE: Proper wiring is essential for the safe operation of this fixture.

GENERAL

You don’t need special tools to install this fixture. Be sure to follow the steps in the order given. Under no circumstances should a fixture be hung on house electrical wires, nor should a swag type fixture be installed on a ceiling, which contains a radiant type heating system. Read instructions carefully. If you are unclear as to how to proceed, consult a qualified electrician.

NOTE: Proper wiring is essential for the safe operation of this fixture.

FIXTURE ASSEMBLY

Carefully removed the fixture from the carton and check that all

parts are included as shown in figure. Be careful not to misplace

any of the screws or parts, which are needed to install this fixture.

INSTALLATION

IMPORTANT: Do not attach fixture directly to outlet box.

STEP 1: take out the socket cluster (V) from the inner frame by loosening the connector (X).

STEP 2: Install the glass panels (S)(T) by carefully placing them inside the inner frame (R) and securing them using the tabs (Z) on the inner frame. (Note: The sticker on the glasses panel with ”outside” should face outward, and should be removed after installing)

STEP 3: Raise the socket cluster (V) against the inner frame (R) and tighten with connector (X)

STEP 4: The hanging pipes for this fixture includes 2 sets of   4pcs X 24", 2pcs X 12", 1pc X 6”, 1pc X 3” of pipes, choose desired installation height. Thread nipple (N) to the pipe (N1). Put the fixture wires through each pipe to be used. Thread all the connected pipes to the fixture connector (P) on the outer frame (Q).

STEP 5: Feed the fixture through canopy (K), and secure swivel (L) to canopy (K) by tightening with wing nuts with washers (J), (I), spring washer (H).

STEP 6: Attach the mounting plate (A) to outlet box with outlet box screws (D), using woodscrews (E) fix the mounting plate (A) to the ceiling making certain the woodscrews (E) fasten into the wooden structure of the building.

GROUNDING INSTRUCTIONS

STEP 1: NEVER CONNECT GROUND WIRE TO BLACK OR WHITE POWER SUPPLY WIRES.

STEP 2: Take note of the color of the wire(s) on your fixture.

Identify which group your fixture wire(s) falls into and connect the wires according to the directions below:

| GROUP A: Connect to Black House Wire | GROUP B: Connect to White House Wire |
| --- | --- |
| BLACK | WHITE |
| *PARALLEL WIRE (round & smooth) | *PARALLEL WIRE (square & ridged) |
| WHITE OR GREY WITH TRACER | WHITE OR GREY WITHOUT TRACER |
| BROWN GOLD OR BLACK WITHOUT TRACER | BROWN, GOLD OR BLACK WITH TRACER |

*NOTE: When parallel wire (SPT-I & SPT-2) is used, the tracer

wire is square shaped or ridged and the less tracer wire is round

in shape or smooth (seen best when viewed from wire end.)

STEP  3:Take  your  fixture  wire(s)  from  group  A  and  place

evenly against the black wire from the outlet box. Do NOT twist wires together before using wire connectors.

STEP 4: Fit a wire connector (not supplied) over the wires and

STEP 5: Connect the fixture wire from group B to the white wire from the outlet box in the same manner. Make sure no bare wires can be seen outside wire connectors.

screw the connector clockwise until you feel a firmness.

If you can pull the connector off, carefully re-do steps 3

and 4, as above, and check again for a firm connection

FINAL ASSEMBLY

STEP 1: After the wires connected, raise canopy (K) so the two mounting screws (B) protrude through the holes on canopy (K) then tighten with cylinder finials (M).

STEP 2: Install bulb (U) to socket (V). (Do not exceed the maximum capacity recommended on the socket.).

CLEANING

To clean, wipe fixture with a soft cloth. Clean glass with a mild soap. Do not use abrasive materials such as scouring pads or powders, steel wool or abrasive paper.

ORDERING PARTS

Keep this sheet for future reference, and in case you need to order replacement parts. All parts for this fixture can be ordered from place of purchase. Be sure to use exact wording from illustration when ordering parts.

Line art shown may not exactly match the fixture enclosed. However, the installations do apply to this fixture.

ITEM NO:802-44L, 802-56L

# Text boxes

802-44L                             802-56L